| Traing Aid | Checklist |
| --- | --- |
| DEPLOYMENT 1.Retrieve vehicle from parking area 2. Retrieve Ancillary equipment from Compound Battery for Generator Tools Tool kit Extender Lubricant Box Wrench Set Box Wrench Ratchet Set Ratchet Set Deep Well Sockets for Antenna U-bolts Battery Operated Ratchet Set Small Sledge Hammer Assorted Tool Set Rags Duct Tape Antenna extenders (4) Antennas (2) Grounding Wires Grounding Stakes Ladder Canopy Tent Tables Chairs Jumper Cables First Aid Kit Fire Extinguisher Gasoline Oil White Board Marker, Cleaner, and Eraser Hand Cleaner Paper Towels Mission Specific Equipment Computers Satellite Phone Optional Equipment and Supplies Case of Water MRE’s Small Refrigerator Microwave Coffee Pot 3. Deploy vehicle to set-up site | DEPLOYMENT Vehicle retrieved from parking area –COMPLETE Pre-deployment Inspection - PDI ELECTRIC EQUIPMENT -LOADED 1.Generator-CHECKED Generator Battery-CHECKED Generator Connect Cord-CHECKED Vehicle Connect Cord-CHECKED Jumper Cables-CHECKED Jumper Box-CHECKED Gasoline (6 Gallons) – CHECKED Oil-CHECKED RADIO EQUIPMENT - LOADED Radios (7)-CHECKED ANTENNA EQUIPMENT - LOADED 1. Antenna Extenders (4) – CHECKED Antennas, Pole (2) –CHECKED Grounding Wires (2) – CHECKED Grounding Stakes (2) – CHECKED Antenna Wires (2) - CHECKED SUPPORT EQUIPMENT - LOADED Tool Kit Extender Lubricant-CHECKED Box Wrench Set-CHECKED Ratchet Set-CHECKED Deep Well Sockets-CHECKED Sledge Hammer-CHECKED Assorted Tool Set-CHECKED Duct Tape-CHECKED Ladder-CHECKED SAFETY EQUIPMENT - LOADED Fire Extinguisher-CHECKED First Aid Kit-CHECKED OFFICE EQUIPMENT - LOADED 1.Tables (2) – CHECKED Chairs (6) – CHECKED Whiteboard-CHECKED Whiteboard Marker,Eraser,Cleaner-CHECKED Pouch (Pens, Pencils, Stapler-CHECKED MISSION SPECIFIC EQUIPMENT - LOADED Computers-CHECKED Print4er - CHECKED Cell Phones-CHECKED Satellite Phone-CHECKED Canopy-CHECKED Western Shelter-CHECKED OPTIONAL EQUIPMENT & SUPPLES - LOADED Refrigerator-CHECKED Microwave-CHECKED Coffee Pot-CHECKED Paper Towels (4) - CHECKED MRE’s-CHECKED Coffee, Creamers, Cups - CHECKED Water (Case) – CHECKED |
| SETUP GENERATOR 1. Deploy Generator and extension cords (100 ft from comm. vehicle) 2. Install Battery 3. Fill Gas Tank 4. Check oil 5. Deploy vehicle extension cord 6. Connect the generator extension cord to the vehicle extension cord 7. Connect the vehicle extension cord to the vehicle power lines 8. Fuel Lever - ON 9. Choke - ON 10. Start Generator 11. Check operation RADIO ANTENNA EQUIPMENT 1. Remove stowed Antenna Equipment 2. Select the 2 bottom Antenna extenders 3. Lubricate narrow end of bottom Antenna Extender and Position one bottom Antenna Extender next to each side holder – NARROW END UP 2. Install Antennas on Antenna extenders 3. Set up ladder 4. Position 1 man on truck roof (roof man) to install Antenna extenders and Antennas 5. Position 1 man on ground (Safety man) to hand Antenna extenders and Antennas to roof man Safety man is responsible for Operational Safety 6. Install 1 Antenna extender in each side holder 7. Install 1 Antenna extender with antenna attached on each Antenna extender 8. Install Ground wire, if necessary 9. Install connecting antenna wire to antenna, if necessary 10.Install connecting antenna wire to radio | SITE SETUP AC POWER Generator-DEPLOYED 100 ft. Extension Cord-DEPLOYED Battery-INSTALLED Gas Tank-FILLED Oil Level-CHECKED Gen. Connect Cord Connected-CONNECTE D Extension Cord-CONNECTED Fuel Lever-ON Choke-ON Generator-START/RUN Generator Operation-Checked Vehicle Connect Cable-CONNECTED RADIO ANTENNA INSTALLATION Antenna Equipment-REMOVED FROM STOWED POSITION Bottom Extenders-LUBRICATED Bottom Extenders-PRE-POSITIONED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible. NOTE Extenders will be pre-positioned with the narrow end in the upright position Antennas Attached to Extenders-ATTACHED Ladder-POSITIONED Antennas and Attached Extenders-PRE-POSITIONED Ground Man positioned at bottom of ladder-POSITIONED NOTE Ground Man is the Safety Man and is responsible for operational Safety Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder. Ground Man hands LEFT side pre-positioned bottom extension to Roof Man -COMPLETED Roof Man inserts LEFT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands RIGHT side pre-positioned bottom extension to Roof Man-COMPLETED Roof Man inserts RIGHT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands LEFT side antennas to Roof Man-COMPLETED Roof Man installs LEFT side antenna extension over bottom extension-INSTALLED Ground Man hands RIGHT side antennas to Roof Man-COMPLETED Roof Man installs RIGHT side antenna extension over bottom extension-INSTALLED Ground Wire-ATTACHED Roof Man descends from truck Roof Safety man provides ladder footing,etcf Left side Antenna wire connected to radio-CONNECTED Right side Antenna wire connected to radio-CONNECTED |
|  | ANCILLARY OPERATIONS |
| OPERATION GENERATOR 1. electrical selector switch – 120v 2. Circuit Breaker - ON 1. Connect generator extension cord to generator 2. Vehicle portable lights - ON RADIO EQUIPMENT 1. Turn on radios | OPERATION AC POWER Generator electrical selector switch to 120v-COMPLETED Generator Circuit Breaker-ON Vehicle Portable Lights-ON NOTE If lights do not come on, check wiring connections, then check bulbs RADIO EQUIPMENT Inverters-ON Radios_ON |
| BREAKDOWN RADIO EQUIPMENT 1. Turn off radios RADIO ANTENNA EQUIPMENT 1. Uninstall connecting antenna wire from radio 2. Set up ladder 3. Position 1 man on truck roof (roof man) to uninstall Antenna extenders and Antennas 4. Position 1 man on ground (safety man) to retrieve Antenna extenders and Antennas from Roof Man 5. Uninstall Ground wire, if necessary 6. Uninstall connecting antenna wire from antenna, if necessary 7. Uninstall 1 Antenna extender with antenna attached on each Antenna extender 8. Uninstall 1 Antenna extender in each side holder – clean debris from end 9. Uninstall Antennas on Antenna extenders 10.Stow Antenna Equipment GENERATOR 1. Generator Circuit Breaker – OFF 2. Uninstall Battery 2. Generator Electrical Selector Switch – OFF 3. Unplug generator extension cord from generator and stow 4. Unplug generator extension cord from extension cord 5. Rewind the vehicle extension cord and stow in comm. vehicle 6. Stow the generator extension cord by attaching to generator 7. Stow the generator in the comm. vehicle | BREAKDOWN RADIO EQUIPMENT Radios-OFF Inverters-OFF |
|  | Right side Antenna wire disconnected from radio-DISCONNECTED Left side Antenna wire disconnected from radio-DISCONNECTED Ground Man positioned at bottom of ladder-POSITIONED Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder Ground Wire-DETACHED Roof Man uninstalls RIGHT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal Roof Man hands RIGHT side antennas to Ground Man-COMPLETED Ground Man positions RIGHT side Antenna against truck-POSITIONED Roof Man uninstalls LEFT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal Roof Man hands LEFT side antennas to Ground Man-COMPLETED Ground Man positions LEFT side Antenna against truck-POSITIONED Roof Man uninstalls RIGHT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands RIGHT side bottom extension to Ground Man-COMPLETED Ground Man positions Bottom Extension against truck-POSITIONED Roof Man uninstalls LEFT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands LEFT side bottom extension to Ground Man –COMPLETED Ground Man positions Bottom Extender against Ttruck.POSITIONED Ground man foots the ladder Roof Man Descends to ground Ladder-REMOVED AND STOWED Bottom Extenders stowed with narrow end visible-STOWED Antenna extenders positioned for disassembly-POSITIONED Antennas removed from Antenna Exxtenders-REMOVED Antenna Extenders stowed with wide end visible-STOWED Antennas-STOWED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible. NOTE Extenders will be pre-positioned with the narrow end in the upright position Antennas Attached to Extenders-ATTACHED NOTE Ground Man is the Safety Man and is responsible for operational Safety WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder. |