DEPLOYMENT Vehicle retrieved from parking area –COMPLETE Pre-deployment Inspection - PDI ELECTRIC EQUIPMENT -LOADED 1.Generator-CHECKED Generator Battery-CHECKED Generator Connect Cord-CHECKED Vehicle Connect Cord-CHECKED Jumper Cables-CHECKED Jumper Box-CHECKED Gasoline (6 Gallons) – CHECKED Oil-CHECKED RADIO EQUIPMENT - LOADED Radios (7)-CHECKED ANTENNA EQUIPMENT - LOADED 1. Antenna Extenders (4) – CHECKED Antennas, Pole (2) –CHECKED Grounding Wires (2) – CHECKED Grounding Stakes (2) – CHECKED Antenna Wires (2) - CHECKED

SUPPORT EQUIPMENT - LOADED Tool Kit Extender Lubricant-CHECKED Box Wrench Set-CHECKED Ratchet Set-CHECKED Deep Well Sockets-CHECKED Sledge Hammer-CHECKED Assorted Tool Set-CHECKED Duct Tape-CHECKED Ladder-CHECKED SAFETY EQUIPMENT - LOADED Fire Extinguisher-CHECKED First Aid Kit-CHECKED OFFICE EQUIPMENT - LOADED 1.Tables (2) – CHECKED Chairs (6) – CHECKED Whiteboard-CHECKED Whiteboard Marker,Eraser,Cleaner-CHECKED Pouch (Pens, Pencils, Stapler-CHECKED

MISSION SPECIFIC EQUIPMENT - LOADED Computers-CHECKED Print4er - CHECKED Cell Phones-CHECKED Satellite Phone-CHECKED Canopy-CHECKED Western Shelter-CHECKED OPTIONAL EQUIPMENT & SUPPLES - LOADED Refrigerator-CHECKED Microwave-CHECKED Coffee Pot-CHECKED Paper Towels (4) - CHECKED MRE’s-CHECKED Coffee, Creamers, Cups - CHECKED Water (Case) – CHECKED

SITE SETUP AC POWER Generator-DEPLOYED 100 ft. Extension Cord-DEPLOYED Battery-INSTALLED Gas Tank-FILLED Oil Level-CHECKED Gen. Connect Cord Connected-CONNECTED Extension Cord-CONNECTED Fuel Lever-ON Choke-ON Generator-START/RUN Generator Operation-Checked Vehicle Connect Cable-CONNECTED

RADIO ANTENNA INSTALLATION Antenna Equipment-REMOVED FROM STOWED POSITION Bottom Extenders-LUBRICATED Bottom Extenders-PRE-POSITIONED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible. NOTE Extenders will be pre-positioned with the narrow end in the upright position Antennas Attached to Extenders-ATTACHED Ladder-POSITIONED Antennas and Attached Extenders-PRE-POSITIONED Ground Man positioned at bottom of ladder-POSITIONED NOTE Ground Man is the Safety Man and is responsible for operational Safety Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder.

Ground Man hands LEFT side pre-positioned bottom extension to Roof Man -COMPLETED Roof Man inserts LEFT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands RIGHT side pre-positioned bottom extension to Roof Man-COMPLETED Roof Man inserts RIGHT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands LEFT side antennas to Roof Man-COMPLETED Roof Man installs LEFT side antenna extension over bottom extension-INSTALLED Ground Man hands RIGHT side antennas to Roof Man-COMPLETED Roof Man installs RIGHT side antenna extension over bottom extension-INSTALLED Ground Wire-ATTACHED Roof Man descends from truck Ground man provides ladder footing - COMPLETED Left side Antenna wire connected to radio-CONNECTED Right side Antenna wire connected to radio-CONNECTED

ANCILLARY OPERATIONS INTENTIONALLY LEFT BLANK

OPERATION AC POWER Generator electrical selector switch to 120v-COMPLETED Generator Circuit Breaker-ON Vehicle Portable Lights-ON NOTE If lights do not come on, check wiring connections, then check bulbs RADIO EQUIPMENT Inverters-ON Radios_ON

BREAKDOWN RADIO EQUIPMENT Radios-OFF Inverters-OFF Right side Antenna wire disconnected from radio-DISCONNECTED Left side Antenna wire disconnected from radio-DISCONNECTED Ground Man positioned at bottom of ladder-POSITIONED Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder Ground Wire-DETACHED Roof Man uninstalls RIGHT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal

Roof Man hands RIGHT side antennas to Ground Man-COMPLETED Ground Man positions RIGHT side Antenna against truck-POSITIONED Roof Man uninstalls LEFT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal Roof Man hands LEFT side antennas to Ground Man-COMPLETED Ground Man positions LEFT side Antenna against truck-POSITIONED Roof Man uninstalls RIGHT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands RIGHT side bottom extension to Ground Man-COMPLETED Ground Man positions Bottom Extension against truck-POSITIONED Roof Man uninstalls LEFT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands LEFT side bottom extension to Ground Man –COMPLETED

Ground Man positions Bottom Extender against Ttruck - POSITIONED Ground man foots the ladder – COMPLETED Roof Man Descends to ground - COMPLETED Ladder-REMOVED AND STOWED Bottom Extenders stowed with narrow end visible-STOWED Antenna extenders positioned for disassembly-POSITIONED Antennas removed from Antenna Exxtenders-REMOVED Antenna Extenders stowed with wide end visible-STOWED Antennas-STOWED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible.