DEPLOYMENT Vehicle retrieved from parking area –COMPLETE Pre-deployment Inspection - PDI ELECTRIC EQUIPMENT -LOADED 1.Generator-CHECKED Generator Battery-CHECKED Generator Connect Cord-CHECKED Vehicle Connect Cord-CHECKED Jumper Cables-CHECKED Jumper Box-CHECKED Gasoline (6 Gallons) – CHECKED Oil-CHECKED RADIO EQUIPMENT - LOADED Radios (7)-CHECKED ANTENNA EQUIPMENT - LOADED 1. Antenna Extenders (4) – CHECKED Antennas, Pole (2) –CHECKED Grounding Wires (2) – CHECKED Grounding Stakes (2) – CHECKED Antenna Wires (2) - CHECKED SUPPORT EQUIPMENT - LOADED Tool Kit Extender Lubricant-CHECKED Box Wrench Set-CHECKED Ratchet Set-CHECKED Deep Well Sockets-CHECKED Sledge Hammer-CHECKED Assorted Tool Set-CHECKED Duct Tape-CHECKED Ladder-CHECKED SAFETY EQUIPMENT - LOADED Fire Extinguisher-CHECKED First Aid Kit-CHECKED OFFICE EQUIPMENT - LOADED 1.Tables (2) – CHECKED Chairs (6) – CHECKED Whiteboard-CHECKED Whiteboard Marker,Eraser,Cleaner-CHECKED Pouch (Pens, Pencils, Stapler-CHECKED MISSION SPECIFIC EQUIPMENT - LOADED Computers-CHECKED Print4er - CHECKED Cell Phones-CHECKED Satellite Phone-CHECKED Canopy-CHECKED Western Shelter-CHECKED OPTIONAL EQUIPMENT & SUPPLES - LOADED Refrigerator-CHECKED Microwave-CHECKED Coffee Pot-CHECKED Paper Towels (4) - CHECKED MRE’s-CHECKED Coffee, Creamers, Cups - CHECKED Water (Case) – CHECKED

SITE SETUP AC POWER Generator-DEPLOYED 100 ft. Extension Cord-DEPLOYED Battery-INSTALLED Gas Tank-FILLED Oil Level-CHECKED Gen. Connect Cord Connected-CONNECTE D Extension Cord-CONNECTED Fuel Lever-ON Choke-ON Generator-START/RUN Generator Operation-Checked Vehicle Connect Cable-CONNECTED RADIO ANTENNA INSTALLATION Antenna Equipment-REMOVED FROM STOWED POSITION Bottom Extenders-LUBRICATED Bottom Extenders-PRE-POSITIONED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible. NOTE Extenders will be pre-positioned with the narrow end in the upright position Antennas Attached to Extenders-ATTACHED Ladder-POSITIONED Antennas and Attached Extenders-PRE-POSITIONED Ground Man positioned at bottom of ladder-POSITIONED NOTE Ground Man is the Safety Man and is responsible for operational Safety Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder. Ground Man hands LEFT side pre-positioned bottom extension to Roof Man -COMPLETED Roof Man inserts LEFT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands RIGHT side pre-positioned bottom extension to Roof Man-COMPLETED Roof Man inserts RIGHT side Bottom Extensions in Truck Side Holding Conduit-COMPLETED Ground Man hands LEFT side antennas to Roof Man-COMPLETED Roof Man installs LEFT side antenna extension over bottom extension-INSTALLED Ground Man hands RIGHT side antennas to Roof Man-COMPLETED Roof Man installs RIGHT side antenna extension over bottom extension-INSTALLED Ground Wire-ATTACHED Roof Man descends from truck Ground man provides ladder footing - COMPLETED Left side Antenna wire connected to radio-CONNECTED Right side Antenna wire connected to radio-CONNECTED

ANCILLARY OPERATIONS

OPERATION AC POWER Generator electrical selector switch to 120v-COMPLETED Generator Circuit Breaker-ON Vehicle Portable Lights-ON NOTE If lights do not come on, check wiring connections, then check bulbs RADIO EQUIPMENT Inverters-ON Radios_ON

BREAKDOWN RADIO EQUIPMENT Radios-OFF Inverters-OFF

Right side Antenna wire disconnected from radio-DISCONNECTED Left side Antenna wire disconnected from radio-DISCONNECTED Ground Man positioned at bottom of ladder-POSITIONED Roof Man Positioned on Truck Roof- POSITIONED WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder Ground Wire-DETACHED Roof Man uninstalls RIGHT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal Roof Man hands RIGHT side antennas to Ground Man-COMPLETED Ground Man positions RIGHT side Antenna against truck-POSITIONED Roof Man uninstalls LEFT side antenna and antenna extension from bottom extension-UNINSTALLED NOTE Ground Man may have to hold bottom extension to facilitate antenna removal Roof Man hands LEFT side antennas to Ground Man-COMPLETED Ground Man positions LEFT side Antenna against truck-POSITIONED Roof Man uninstalls RIGHT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands RIGHT side bottom extension to Ground Man-COMPLETED Ground Man positions Bottom Extension against truck-POSITIONED Roof Man uninstalls LEFT side Bottom Extensions from Truck Side Holding Conduit-UNINSTALLED Roof Man hands LEFT side bottom extension to Ground Man –COMPLETED Ground Man positions Bottom Extender against Ttruck.POSITIONED Ground man foots the ladder – COMPLETED Roof Man Descends to ground - COMPLETED Ladder-REMOVED AND STOWED Bottom Extenders stowed with narrow end visible-STOWED Antenna extenders positioned for disassembly-POSITIONED Antennas removed from Antenna Exxtenders-REMOVED Antenna Extenders stowed with wide end visible-STOWED Antennas-STOWED NOTE Bottom Extenders are stowed with the wide end visible. The Antenna Extenders are stowed with the narrow end visible. NOTE Extenders will be pre-positioned with the narrow end in the upright position Antennas Attached to Extenders-ATTACHED NOTE Ground Man is the Safety Man and is responsible for operational Safety WARNING Ladder climbing can be hazardous. Always exercise extreme caution when climbing and when transferring from the ladder to the roof. Always use a safetyman to foot the bottom of the ladder.