|  | TK270G |
| --- | --- |
|  | SETUP |
| 1 | Connect Serial to USB |
| 2 | Plug USB into computer |
| 3 | Plug 2 pin into radio |
| 4 | Run KPG56 D program |
| 5 | Click “My Computer” click “Device Manager” Shows serial Port & Comm Port Bring program back up Input Comm Port Setup Highlight Comm Port Insert Listed Comm Port |
| 6 | Radio start |
| 7 | Model/model info |
| 8 | Select Dropdown box -128 ch E Portable VHF TK 270 G 146 – 174 OK/OK |
| 9 | Skip for now |
| 10 | Program/Read from rdio/Read/015 ?? (will give freqs) |
|  | TK 2312 |
|  | Start/all programs/kenwood fpu |
|  | Select KBG 134D |
|  | Bring up program |
|  | Input Comm Port Setup Highlight Comm Port Insert Listed Comm Port |
|  | Radio start |
|  | Model/model info |
|  | Select Dropdown box -128 ch E Portable VHF TK 2312 (choose “K”) 146 – 174 OK/OK |
|  | Skip for now |
|  | Program/Read from rdio/Read/OK (will give freqs) |
|  | TK 7360 |
|  | Start/all programs/kenwood fpu |
|  | Select KBG 135D |
|  | Bring up program |
|  | Connect adio Inerce cse to prolific SRB – Serial |
|  | Connect to Rdio |
|  | Input Comm Port Setup Highlight Comm Port Insert Listed Comm Port |
|  | Radio start |
|  | Model/model info |
|  | Select Dropdown box -128 ch E Portable VHF TK 7360 146 – 174 OK/OK |
|  | Skip for now |
| *** | Program/Read from rdio/Read/OK (will give freqs) |

|  | ADD/ DELET/ CHANGE |
| --- | --- |
|  | Channel edit button is ALTER/ DELETE/ ADD |
| 1 | Select channel (highlight) |
| 2 | Ch edit button |
|  | To APPLY |
|  | File |
|  | Save (saves program) |
|  | WRITE TO RADIO |
|  | Program |
|  | Write to radio |
|  | Drop down box write |