Specifications and options.

Model TK-7360HV TK-8360HU

GENERAL

Frequency Range 136~174 MHz 450~520 MHz

Number of Channels Zone Max.128 per Radio

Channel Max.128 per Zone

Channel Spacing

Wide 25 kHz 25 kHz

Narrow 12.5 kHz 12.5 kHz

Operating Voltage 13.6 V DC±15 %

Current Drain

Standby 0.4 A 0.4 A

Receive 1.0 A 1.0 A

Transmit 14.0 A 14.0 A

Operating Temperature Range -22 ºF ~ +140 ºF (-30 ºC ~ +60 ºC)

Frequency Stability ±2.5 ppm (-22 ºF ~ +140 ºF)

Antenna Impedance 50 Ω

Channel Frequency Spread 38 MHz 70 MHz

Dimensions (W x H x D), 6.3” x 1.7” x 5.4”

Projections not included (160 mm x 43 mm x 137 mm)

Weight (net) 2.6 lbs. (1.18 kg)

FCC ID K44415401 K44415502

Model TK-7360HV TK-8360HU

RECEIVER (Measurements made per EIA/TIA-603)

Sensitivity (12dB SINAD)

Wide 0.28 μV

Narrow 0.35 μV

Selectivity

Wide 75 dB

Narrow 65 dB

Intermodulation Distortion

Wide 70 dB

Narrow 65 dB

Spurious Response 75 dB

Audio Output

(4 Ω Impedance) 4 W with less than 5 % distortion

TRANSMITTER (Measurements made per EIA/TIA-603)

RF Output Power 5 W / 25 W / 50 W 5 W / 25 W / 45 W*1

Spurious Response 70 dB

Type of Emission

Wide 16K0F3E

Narrow 11K0F3E

FM Hum & Noise

Wide 45 dB

Narrow 40 dB

Microphone Impedance 600 Ω

Audio Distortion

Wide 3 %

Narrow 5 %

Kenwood follows a policy of continuous advancement in development.

For this reason specifications may be changed without notice.

*1: 490 ~ 512 MHz: 5/25/40 W, 512 ~ 520 MHz: 5/25/35 W

FleetSync® is a registered trademark of Kenwood Corporation.

Windows® is a registered trademark of Microsoft Corporation in the United States and other countries.

All other trademarks are property of their respective owners.

􀀀 KMC-35

Microphone

(Supplied)

􀀀 KMC-36

Microphone

with Keypad

􀀀 KMC-9C

Desktop Microphone

􀀀 KES-3

External Speaker

􀀀 KES-5

External Speaker

(requires KCT-60 option)

􀀀 KMB-10

Key Lock Adapter

􀀀 KLF-2

Line Filter

􀀀 KCT-18

Ignition Sense Cable

(requires KCT-60 option)

􀀀 KCT-36

3m Extension Cable

(for KCT-60)

􀀀 KCT-60

DB 15-to-15 Pin

Molex Adaptor Cable

􀀀 VGS-1

Voice Storage Unit

(uses 26p connector)

Standard MIL 810C MIL 810D MIL 810E MIL 810F MIL 810G

Methods/Procedures Methods/Procedures Methods/Procedures Methods/Procedures Methods/Proced