### BCREPC HAZARDOUS MATERIAL PLAN

ANNEX M: EMERGENCY FIRE SERVICES - WATER SUPPLY MANAGER CHECKLIST

| ITEM | ACTIONS | ( |
| --- | --- | --- |
| 1 | Keep the Incident Commander apprised of progress made in establishing a water supply, any problems that are encountered, and the status of the supply once it has been established. |  |
| 2 | Monitor all water sources by checking residual pressure at hydrants, levels in tanks, or levels in water ponds. If there is more than one relay operation, appoint a Relay Control Officer (RCO) to oversee each relay. |  |
| 3 | Notify water systems personnel to provide maximum production for extended operations. |  |
| 4 | Prepare to provide a supplemental supply if increased flow is required or if the stored supply is depleted. |  |
| 5 | Estimate the required water flow |  |
| 6 | Monitor fuel levels for all water-source apparatus |  |
| Incident Location |  |
| Date |  |
| Water Supply Officer |  |
| Engines / Supply |  |
| ITEM | FIRE HYDRANTS AS A WATER SOURCE |
| 1. | Hydrant Map / Distribution System: | ( |
|  | Primary feeder: 16” to 60” |  |
|  | Secondary feeder: 12’ to 14” |  |
|  | Distributor feeder: 8” or less |  |
| 2. | Water Lines: | ( |
|  | Single line: Dead end |  |
|  | Loop: fed from two directions |  |
|  | Grid: fed from four directions |  |

### BCREPC HAZARDOUS MATERIAL PLAN

ANNEX M: EMERGENCY FIRE SERVICES - WATER SUPPLY MANAGER CHECKLIST (cont.)

| FIRE HYDRANTS AS A WATER SOURCE (cont.) |
| --- |
| 3. | Water System: | ( |
|  | Gravity supply (elevated) |  |
|  | Direct pumping (high efficiency) |  |
|  | Combination |  |
| 4. | Hydrant Colors: | ( |
|  | Light Blue: 1500 GPM or more |  |
|  | Green: 1000 to 1500 GPM |  |
|  | Orange: 500 to 1000 GPM |  |
| WATER SUPPLY MANAGER (cont.) |
|  | Red: less than 500 GPM |  |
| ITEM | PRIVATE WATER SUPPLY SYSTEM | ( |
| 1. | Size of Water Line: |
| 2. | Tank Capacity / Gallons: |
| 3. | Location of Fire Pump: |
| 4. | Pump GPM: |
| 5. | Auxiliary Water Supplies: |
| 6. | Mobile Water Supply: |
| 7. | Commercial tank Trucks: |
| 8. | Streams: |
| 9. | Ponds: |
| 10. | Lakes: |
| 11. | Swimming Pools: |
| 12. | Irrigation Systems: |
| 13. | Stockyards: |
| 14. | Sewage Treatment Plants: |
| 15. | Railroad Tank Cars |
| RELAY OPERATIONS FORMULA: |
| Relay Distance ------------------------------- + One Attack Pumper = Total Number of Pumpers Distance From (See Table) |

### BCREPC HAZARDOUS MATERIAL PLAN

ANNEX M: EMERGENCY FIRE SERVICES - WATER SUPPLY MANAGER CHECKLIST (cont.)

| MAXIMIM DISTANCE OF WATER FLOW AT 180 PSI (IN FEET)* |
| --- |
| FLOW GPM | HOSE DIAMETER IN INCHES |
|  | 2.5 | 3 | 4 | 5 | 6 |
| 100 | 9000 | 22500 | 90000 | 225000 | 360000 |
| 200 | 2250 | 5625 | 22500 | 56250 | 90000 |
| 250 | 1440 | 3600 | 14400 | 36000 | 57600 |
| 300 | 1000 | 2500 | 10000 | 25000 | 40000 |
| 400 | 563 | 1406 | 5625 | 14060 | 22500 |
| 500 | 360 | 900 | 3600 | 9000 | 14400 |
| 750 | 160 | 400 | 1600 | 4000 | 6400 |
| 1000 | 90 | 225 | 900 | 2250 | 3600 |
| TANKER WATER SHUTTLE: Calculating Continuous Flow Capacity** |
| V (Tanker Capacity) -------------------------- = Q (GPM) A + 2T + B V=Capacity in usable water (determined in unloading test) A=Unloading time (in test) + 75 minutes for handling B=Loading time (in test) + .75 minutes for handling 2T=Travel time for desired location Example: T=1 mile @ 30 mph = 2 minutes X 2 for round trip |
| * Fire Department Pumping Apparatus, 7th Ed., IFSTA, pg. 149 ** The Fire Department Water Supply Handbook, Eckman, William F., Engineering Books and Videos, pg. 115 |